## Slide 1
Authors’ name (email@uec.ac.th)
Your Affiliation（ex: Graduate School of Informatics and Engineering, The University of Electro-Communications, 1-5-1 Chofugaoka Chofu-city, Tokyo, Japan.
To improve the bit-error rate (BER) of an ultra-high densities bit-patterned magnetic recording (BPMR) systems, the inter-symbol interference (ISI) and inter-track interference (ITI) effects resulting from the reduction of spacing between bit islands in the along- and across-track directions must be efficiently handled. Array-reader based BPMR is considered as a key technology for next-generation magnetic recording due to its advantages such as diversity gain against noise and inter-track interference cancellation. Therefore, we propose a three-reader four-track (3R4T) system where a rate-3/4 two-dimensional (2D) modulation code and ITI subtraction technique are used to improve recording system performance. Moreover, the 2D detector is also modified according with the ITI subtraction technique, which not only leads to have lower complexity but also yields better BER performances. Simulation results demonstrate that significant performance gain under position and size fluctuation effects can be achieved using our proposed system.
Introduction
In this paper, we propose a simple rate-3/4 two-dimensional (2D) modulation code which operates together with the ITI subtraction technique. Moreover, we also propose the modified 2D detector that accordingly performs together with both proposed modulation code and ITI subtraction technique. Then, all three proposed methods will be jointly operated under the array-reader based BPMR system.
An Rate-3/4 2D Modulation Encoding
For the rate-3/4 2D modulation encoding, the three user data sequences with the length of 4096 bits is encoded to be four encoded data sequences before recording onto the medium. The second user data sequence is copied, the replica sequence is then defined as the redundant data sequence which will be recorded onto the third track in the medium as shown in Fig. 1 (top). While, the first, second and third user data sequences will be recorded onto the first, second and fourth tracks, respectively. In this work, three readers are used to read four recorded data sequences. The first and third readers are placed at the center of the first and fourth track, respectively. Although, the second reader is positioned between the second and third tracks as depicted in Fig 1 (bottom).
An ITI Subtraction Technique
Due to the size of this track, i.e., the combination of the second and third tracks, is twice bigger than the normal track size, which implies that the second readback signal that is obtained from the second reader can provide the high reliability. Therefore, we can utilize this data sequence to subtract the ITI effects of the first and third readback signals in order to increase the first and forth track performances, respectively. For ITI subtracting process, the second readback sequence is fedback to convolute with ideal target coefficient to produce the remaining side-track ITI sequences before subtracting with both first and third readback sequences as shown in Fig. 2.
Proposed Scheme
Simulation Results
Acknowledgment
Add the name of your paper: The poster size must be A1
The uploaded poster link will be sent the authors through authors’ e-mail
Fig. 1. The regular bit-patterned media with an array-reader under AD of 3.0 Tb/in2. Three readers are used to read four data tracks immediately. Here, the bit-islands were constructed without (top) and with 5% position and size fluctuations (bottom).
Fig. 2. Block diagram of the transmitter and receiver of the three-reader four-track (3R4T) BPMR system which consists of the proposed 3/4 2D modulation encoder, ITI subtraction technique, and modified 2D Viterbi algorithms.
Fig. 3. SNR requirement to achieve BER = 10-4 dB comparison as a function of various ADs without and with 5% position and size fluctuation effects.
This work was supported by Thailand Research Fund (TRF) under the grant number RSA6080051 and King Mongkut’s Institute of Technology Ladkrabang, Thailand.
In this work, we consider all four systems to evaluate the proposed methods which consist of 1) the “Conventional System,” i.e., the system operates without any coding, ITI subtraction and modified 2D detector 2) the “5/6 Mod System,” i.e., the system operates by using the rate-5/6 2D modulation code, ITI subtraction and 2D detector 3) the “Proposed System II” means the system operates by using the rate-3/4 2D modulation code, ITI subtraction and 2D detector 4) the “Proposed System I” operates same as the previous system but the modified 2D detector is instead used the normal one.
Here, we separate the consideration into two cases, the recording system without and with 5% position and size fluctuations. As shown in Fig. 3, it is clear that the proposed systems can provide the lower signal-to-noise ratio (SNR) to achieve BER = 10-4 than the rate-5/6 2D modulation code and conventional systems for all ADs. Moreover, it seems that both proposed systems yield higher performance gain especially at the higher ADs. In addition, when we compare their performances under the same user density (UD), UD = ADXR, where R is code rate, the proposed systems still provide better performances over the other systems.
UEC Workshop 2025